## Slide 1
Behind-the-Meter Solar + Storage
Investment Summary
Acme Industries
123 Solar Way, San Jose, CA 95131 | 1234567890
Confidential | February 2026

## Slide 2
Executive Summary
Acme Industries | PG&E B-19 TOU | 150 kW-DC Solar + 200 kWh BESS
Day-1 savings of $18K (50.6%) with zero upfront capital. System offsets 60% of annual load and provides long-term rate certainty.
FINANCIAL OVERVIEW
Current Annual Utility Bill
$35K
Projected Year 1 Cost (w/ Solar)
$17K
Year 1 Net Savings
$18K
Savings Rate
50.6%
PPA Rate (Year 1)
$0.105/kWh
PPA Escalator
1.5%/yr
Contract Term
25 years
Upfront Cost
$0
SYSTEM & ENERGY
System Size (DC)
150 kW
Annual Production
87 MWh
Annual Load
145 MWh
Solar Offset
60%
Specific Yield
578 kWh/kW
Self-Consumption
88%
Peak Demand
0 kW
Battery Storage
200 kWh
Source: 38DN pv-rate-sim billing model; 8,760-hour simulation
38 DEGREES NORTH | CONFIDENTIAL
1 / 11

## Slide 3
Exhibit 1: Acme Industries spends $35K/yr on electricity (B-19 TOU)
PG&E | 145 MWh annual load | 0 kW peak demand | $0.2414/kWh blended rate
All-in blended rate of $0.2414/kWh. Demand charges represent a significant cost component. Rising utility rates compound exposure annually.
$35K
Annual Utility Bill
0 kW
Peak Demand
$0.2414
Blended $/kWh
145 MWh
Annual Load
MONTHLY COST BREAKDOWN (WITHOUT SOLAR)
Month | Load (MWh) | Peak kW | Energy ($) | Demand ($) | Fixed ($) | Total ($)
Jan | 8.5 | 0 | $1,400 | $650 | $150 | $0
Feb | 7.8 | 0 | $1,400 | $650 | $150 | $0
Mar | 9.2 | 0 | $1,400 | $650 | $150 | $0
Apr | 10.5 | 0 | $1,400 | $650 | $150 | $0
May | 12.0 | 0 | $1,400 | $650 | $150 | $0
Jun | 14.5 | 0 | $1,400 | $650 | $150 | $0
Jul | 16.0 | 0 | $1,400 | $650 | $150 | $0
Aug | 15.5 | 0 | $1,400 | $650 | $150 | $0
Sep | 13.0 | 0 | $1,400 | $650 | $150 | $0
Oct | 11.0 | 0 | $1,400 | $650 | $150 | $0
Nov | 9.0 | 0 | $1,400 | $650 | $150 | $0
Dec | 8.0 | 0 | $1,400 | $650 | $150 | $0
Source: 38DN billing simulation; PG&E B-19 TOU rate schedule; 8,760-hour model
38 DEGREES NORTH | CONFIDENTIAL
2 / 11

## Slide 4
Exhibit 2: Proposed 150 kW solar + 200 kWh storage at zero upfront cost
System sized to optimize load offset and demand charge reduction under current tariff structure
SOLAR ARRAY (PV)
DC Capacity
150 kW
AC Interconnection
125 kW
DC:AC Ratio
1.2:1
BATTERY STORAGE (BESS)
Energy Capacity
200 kWh
Power Rating
50 kW
Duration
4.0 hours
PPA Rate: $0.105/kWh | Escalator: 1.5%/yr | Term: 25 years | Upfront Cost: $0 | Tariff: B-19 TOU Option R
38 DEGREES NORTH | CONFIDENTIAL
3 / 11

## Slide 5
Exhibit 3: Solar reduces Year 1 electricity cost by $18K (50.6%)
Comparison at current B-19 TOU rates | Savings accrue from Day 1
YEAR 1 COST COMPARISON
Without Solar (B-19 TOU)
$35K
per year
With Solar + Storage
$17K
per year
NET SAVINGS: $18K / YEAR (50.6%)
YEAR 1 SAVINGS BREAKDOWN
Energy charge reduction
$6K
Demand charge reduction
$3K
Export credits
$-800
NBC charges (NEM-2)
($200)
ANNUAL SAVINGS BY COMPONENT
Chart: Contract Year
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Energy Savings | 5.8 | 6.032 | 6.2464 | 6.4425 | 6.6196 | 6.7768 | 6.9135 | 7.0288 | 7.1217 | 7.1916 | 7.2373 | 7.258 | 7.2526 | 7.2202 | 7.1596 | 7.0696 | 6.9492 | 6.7971 | 6.612 | 6.3927 | 6.1376 | 5.8456 | 5.5149 | 5.1441 | 4.7317
Demand Savings | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6 | 2.6
Export Credits | 0.8 | 0.832 | 0.86528 | 0.89989 | 0.93589 | 0.97332 | 1.0123 | 1.0527 | 1.0949 | 1.1386 | 1.1842 | 1.2316 | 1.2808 | 1.3321 | 1.3853 | 1.4408 | 1.4984 | 1.5583 | 1.6207 | 1.6855 | 1.7529 | 1.823 | 1.8959 | 1.9718 | 2.0506
NBC Charges | -0.2 | -0.208 | -0.21632 | -0.22497 | -0.23397 | -0.24333 | -0.25306 | -0.26319 | -0.27371 | -0.28466 | -0.29605 | -0.30789 | -0.32021 | -0.33301 | -0.34634 | -0.36019 | -0.3746 | -0.38958 | -0.40516 | -0.42137 | -0.43822 | -0.45575 | -0.47398 | -0.49294 | -0.51266
Current NEM regime: NEM-2
Savings grow each year as utility rates escalate while the solar cost remains contractually fixed.
Source: 38DN billing simulation at current published tariff rates
38 DEGREES NORTH | CONFIDENTIAL
4 / 11

## Slide 6
Exhibit 4: Cumulative savings reach $0 over 25 years
Illustrative projection at 4%/yr utility escalation | PPA at $0.105/kWh, 1.5%/yr escalator
At a conservative 4%/yr utility escalation, cumulative savings exceed $0. Actual historical rate growth has been materially higher.
Year | Utility Cost (No Solar) | Total Cost (w/ Solar) | Annual Savings | Savings % | Cumulative Savings
1 | $35K | $17K | $18K | 50.6% | $0
2 | $36K | $18K | $19K | 51.5% | $0
3 | $38K | $18K | $20K | 52.5% | $0
5 | $41K | $19K | $22K | 54.3% | $0
10 | $50K | $21K | $29K | 58.5% | $0
15 | $61K | $23K | $38K | 62.3% | $0
20 | $74K | $25K | $49K | 65.8% | $0
25 | $90K | $28K | $62K | 69.0% | $0
Source: 38DN projection model | Assumes 4%/yr linear utility rate escalation. PPA rate of $0.105/kWh at 1.5%/yr is contractually fixed.
38 DEGREES NORTH | CONFIDENTIAL
5 / 11

## Slide 7
Exhibit 5: Solar offsets 60% of site load (88% self-consumed)
87 MWh annual production | 145 MWh annual load | 11 MWh exported to grid
MONTHLY PRODUCTION VS LOAD
Chart: MWh
| Jan | Feb | Mar | Apr | May | Jun | Jul | Aug | Sep | Oct | Nov | Dec
Site Load (MWh) | 8.5 | 7.8 | 9.2 | 10.5 | 12 | 14.5 | 16 | 15.5 | 13 | 11 | 9 | 8
Solar Production (MWh) | 4.2 | 5.1 | 6.8 | 8.5 | 9.8 | 10.5 | 10.2 | 9.5 | 7.8 | 6 | 4.5 | 3.8
60%
Solar Offset
87 MWh
Annual Production
88%
Self-Consumption
578
Specific Yield (kWh/kW)
Source: 38DN 8,760-hour simulation; monthly aggregation of hourly production and load profiles
38 DEGREES NORTH | CONFIDENTIAL
6 / 11

## Slide 8
Exhibit 6: System produces 87 MWh/yr, offsetting 60% of site load
Yield: 578 kWh/kW | Self-consumption: 88% | Export: 11 MWh
87 MWh
Annual Production
145 MWh
Annual Load
60%
Solar Offset
88%
Self-Consumption
MONTHLY ENERGY & BILLING SUMMARY (YEAR 1)
Month | Load (MWh) | Solar (MWh) | Import (MWh) | Export (MWh) | Peak kW | Energy ($) | Demand ($) | Export Cr. ($) | Net Bill ($)
Jan | 8.5 | 4.2 | 5.0 | 0.7 | 0 | $0 | $0 | $0 | $0
Feb | 7.8 | 5.1 | 3.5 | 0.8 | 0 | $0 | $0 | $0 | $0
Mar | 9.2 | 6.8 | 3.2 | 0.8 | 0 | $0 | $0 | $0 | $0
Apr | 10.5 | 8.5 | 3.0 | 1.0 | 0 | $0 | $0 | $0 | $0
May | 12.0 | 9.8 | 3.5 | 1.3 | 0 | $0 | $0 | $0 | $0
Jun | 14.5 | 10.5 | 5.5 | 1.5 | 0 | $0 | $0 | $0 | $0
Jul | 16.0 | 10.2 | 7.2 | 1.4 | 0 | $0 | $0 | $0 | $0
Aug | 15.5 | 9.5 | 7.2 | 1.2 | 0 | $0 | $0 | $0 | $0
Sep | 13.0 | 7.8 | 6.2 | 1.0 | 0 | $0 | $0 | $0 | $0
Oct | 11.0 | 6.0 | 5.8 | 0.8 | 0 | $0 | $0 | $0 | $0
Nov | 9.0 | 4.5 | 5.2 | 0.7 | 0 | $0 | $0 | $0 | $0
Dec | 8.0 | 3.8 | 4.8 | 0.6 | 0 | $0 | $0 | $0 | $0
TOTAL | 145.0 | 86.7 | 59.8 | 10.8 | — | $11,000 | $5,200 | $0 | $17,300
Source: 38DN 8,760-hour billing simulation | All values Year 1
38 DEGREES NORTH | CONFIDENTIAL
7 / 11

## Slide 9
Process Overview
From proposal to commercial operation
1
System Installation
150 kW solar with 200 kWh battery installed on-site at zero cost to you.
2
Tariff Optimization
Transition to the optimal PG&E rate schedule that maximizes value from BTM generation.
3
Solar Feeds Operations Directly
Production consumed on-site first, reducing grid imports during daylight hours. Excess charges the battery.
4
Battery Dispatches During Peak Hours
50 kW battery discharges during expensive on-peak periods, shaving demand charges.
5
Predictable, Fixed-Rate Energy
PPA at $0.105/kWh, 1.5%/yr escalator for 25 years. No rate volatility on solar kWh.
System owned, operated, and maintained by 38 Degrees North for the full 25-year term. Zero operational risk or cost to host.
38 DEGREES NORTH | CONFIDENTIAL
8 / 11

## Slide 10
Exhibit 7: Fixed-rate PPA hedges against rising utility costs
PG&E | Rate certainty as a strategic advantage
The PPA provides a contractually fixed energy cost for 25 years. Day-1 savings are locked in; future utility increases widen the margin.
Chart: Contract Year
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
Utility Only @ 10%/yr | 35 | 38.5 | 42.35 | 46.585 | 51.2435 | 56.3679 | 62.0046 | 68.2051 | 75.0256 | 82.5282 | 90.781 | 99.8591 | 109.845 | 120.8295 | 132.9124 | 146.2037 | 160.8241 | 176.9065 | 194.5971 | 214.0568 | 235.4625 | 259.0087 | 284.9096 | 313.4006 | 344.7406
Utility Only @ 7%/yr | 35 | 37.45 | 40.0715 | 42.8765 | 45.8779 | 49.0893 | 52.5256 | 56.2024 | 60.1365 | 64.3461 | 68.8503 | 73.6698 | 78.8267 | 84.3446 | 90.2487 | 96.5661 | 103.3257 | 110.5585 | 118.2976 | 126.5785 | 135.439 | 144.9197 | 155.0641 | 165.9185 | 177.5328
Utility Only @ 4%/yr | 35 | 36.4 | 37.856 | 39.3702 | 40.945 | 42.5829 | 44.2862 | 46.0576 | 47.8999 | 49.8159 | 51.8085 | 53.8809 | 56.0361 | 58.2776 | 60.6087 | 63.033 | 65.5543 | 68.1765 | 70.9036 | 73.7397 | 76.6893 | 79.7569 | 82.9472 | 86.265 | 89.7156
With PPA + Solar | 17.3 | 17.7644 | 18.244 | 18.7393 | 19.2509 | 19.7794 | 20.3253 | 20.8895 | 21.4725 | 22.075 | 22.6978 | 23.3416 | 24.0072 | 24.6953 | 25.407 | 26.1429 | 26.9041 | 27.6915 | 28.506 | 29.3487 | 30.2206 | 31.1229 | 32.0567 | 33.0232 | 34.0236
SCENARIO ASSUMPTIONS
• Middle case: 4%/yr utility escalation
• Upper case: 7%/yr utility escalation
• Stress case: 10%/yr utility escalation
• PPA: $0.105/kWh, 1.5%/yr escalator
• Grid residual escalated at 4%/yr
• Term: 25 years
KEY CONSIDERATIONS
• Wildfire liability, grid hardening, and transmission costs drive rates upward
• Regulatory cost recovery provides limited customer rate relief
• PPA rate is contractually fixed for the full 25-year term
• Day-1 economics are positive at current rates
Source: 38DN projection model; PG&E published tariff rates; illustrative scenarios
38 DEGREES NORTH | CONFIDENTIAL
9 / 11

## Slide 11
Next Steps
1
Execute Letter of Intent
Non-binding LOI confirms mutual interest and key commercial terms.
2
Site Assessment & Engineering
Engineering conducts site visit; confirms layout, interconnection, and structural feasibility.
3
Execute PPA
Finalize 25-year PPA at $0.105/kWh with 1.5% annual escalator.
4
Permitting & Construction
38DN manages all permits, utility coordination, and construction.
5
Commercial Operation
System goes live. Savings begin immediately.
Lock in rate certainty. Zero upfront investment.